## Slide 1: Microprogrammed Embedded Systems
Tic-Tac-Tile
Lucas Jung @gruvw
01 / 2024

## Slide 2: NDS features: checklist (1/4)
ARM Processors
  ARM9 to control the two screens, the buttons (Left, Right, Up, Down, A, Start, Select), send IPC messages to ARM7 to control sound and Wi-Fi.
  ARM7 for audio, touchscreen and Wi-Fi.
Timers / Interrupts
  Timer 0: variable speed, game time progress bar.
  Timer 1: FREQ_64(60), game state FSM update.
  Timer 2: TIMER_FREQ_64(10), button debounce, Wi-Fi spam prevention.

## Slide 3: NDS features: checklist (2/4)
Graphics
  Main display: Mode 5 with backgrounds 2 and 3 (ext. rotoscale), used to display the game pieces, and the board background + begin menu.
  Sub display: Mode 5 with backgrounds 0 (tiled mode) and 2 (ext. rotoscale), used to display the settings selection + progress bar, and the game over screen.
Keypad
  Controlling the top game board actions (interrupts):
    Left, Right, Up, Down = Move selected cell
    A = Place piece on selected cell
    Start = Start, Terminate, Restart game
    Select = Reinitiate NDS pairing (Wi-Fi)

## Slide 4: NDS features: checklist (3/4)
Touchscreen
  Select the game settings in the beginning menu, 6 different touch areas used, select game difficulty (speed) and game mode.
  Reading touchscreen by polling.
Sound
  There is a background music (MOD format) in the menu.
  Another background music (MOD format) is playing during a game. It will speed up depending on the selected game difficulty.
  Playing 3 sound effects (WAV format): when selecting a setting in the menu, when placing a piece on the board, and at the end of the game.

## Slide 5: NDS features: checklist (4/4)
Sprites
  7 sprites in the project: 4 sprites are used to display the outcome of the game on the Game Over screen: (1) crown for the winner, each side (2) has their sprite, (1) clock to indicate losing because of timer; 3 sprites indicate the status of the NDS connection/pairing (Wi-Fi).
Wi-Fi
  Wi-Fi connection with AP is used to communicate between two NDS and play two player games.
  Designed and implemented P2P-BOP protocol to pair two NDS.
  Designed and implemented Message Queue and ACK system to avoid packet loss.
  Added simultaneous message action recovery mechanism
See project README for more details!

## Slide 6: NDS Wi-Fi P2P-BOP

## Slide 7: NDS Wi-Fi Message Queue

## Slide 8: NDS project screenshot
Include an image with the final view/s of your project on the actual NDS device